## Slide 1: 第三章 图像增强
童立靖
北方工业大学计算机学院
tong_lijing@163.com

## Slide 2
目 录
伪彩色处理
假彩色处理

## Slide 3: Pseudocolor Image Processing 伪彩色处理
Notion:The pseudo-colors used to colorize a gray level image do not represent the original, true colors if there were originally a color image. One of the principal motivations for using false-color is the fact that humans can discern thousands of color shades and intensities, compared to only two dozen or so shaded of gray.
概念：为了更好地观察和解释图像中不同灰度级的内容，人为地把不同的颜色分配到单色图像(可能来自某个真彩图像)上。实例：
Notes: pseudo
/ ˈsjuːdəu; US ˈsuː-; ˋsudo/ adj (infml 口) not genuine; sham or insincere 假的; 虚伪的; 不真诚的: This apparent interest of his in modern music is completely pseudo. 他对现代音乐显露出的雅兴纯属自欺欺人.

## Slide 4
Notes: 低频信号，灰度感知强
高频信号，彩色感知强。

## Slide 12
Notes: 光线微弱时，灰度感知强
光线明显时，彩色感知强。

## Slide 13: 伪彩色增强基本原理
由于人眼分辨不同彩色的能力比分别不同的灰度级的能力强，因此，把人眼无法区别的灰度变化，施以不同的彩色来提高识别率，这便是伪彩色增强的基本依据。

## Slide 14: 伪彩色增强基本思路
要由灰度图像生成一幅彩色图像是一个到三个的映射。
显然由少信息量获得多信息量必然是基于估计原理。也就是说，对未知的部分，通过各种手段进行合理的估计。
研究的目的不同，则给出的灰度到彩色的估计映射方法也随之不同。

## Slide 15: 伪彩色增强方法分类
伪彩色增强方法大致可以分为以下三类：
基于区域分割的伪彩色方法
基于灰度调色板的伪彩色方法
基于灰度变换的伪彩色方法

## Slide 16: 基本原理
这是一种对不同的区域进行不同颜色增强的方法。
目的是，可同时增强并清晰地观察不同区域的细节。

## Slide 17: 应用领域与实现方法
这种伪彩色技术在医学诊断中常被用到，目的是突出病灶，提高诊断率。
该伪彩色技术是对原图进行了预处理，将识别出属于不同性质的区域给不同的色彩。

## Slide 18: 示 例

## Slide 19: 伪彩色增强方法分类
伪彩色增强方法大致可以分为以下三类：
基于区域分割的伪彩色方法
基于灰度调色板的伪彩色方法
基于灰度变换的伪彩色方法

## Slide 20: 基本原理
索引值 | R | G | B
1 | R1 | G1 | B1
2 | R2 | G2 | B2
： | : | : | :
N | RN | GN | BN
按照位图文件的索引色模式，首先根据需要设计一个调色板。然后，将灰度值作为调色板的索引值，完成从灰度到彩色的映射。
灰
度
值

## Slide 21: 映射关系
索引值 | R | G | B
1 | R1 | G1 | B1
2 | R2 | G2 | B2
： | : | : | :
N | RN | GN | BN
索引值 | R | G | B
1 | R1 | G1 | B1
2 | R2 | G2 | B2
： | : | : | :
N | RN | GN | BN

## Slide 22: 调色板的设计
调入某个彩色图像的调色板，作为伪彩色映射用的灰度调色板。

## Slide 23: 调色板映射例

## Slide 24: 调色板映射例

## Slide 25: 伪彩色增强方法分类
伪彩色增强方法大致可以分为以下三类：
基于区域分割的伪彩色方法
基于灰度调色板的伪彩色方法
基于灰度变换的伪彩色方法

## Slide 26
Intensity Slicing and Color Coding
强度分层与颜色编码
The pseudo-colors used to colorize a gray level image do not represent the original, true colors if there were originally a color image. One of the principal motivations for using false-color is the fact that humans can discern thousands of color shades and intensities, compared to only two dozen or so shaded of gray.
其中l0 表示黑色
lL-1表示白色
例:

## Slide 27
Pseudocolor Image Processing
Intensity Slicing 强度分层
Binary Image

## Slide 28
Assign one color to the brightest gray-level and another to all other gray levels.
内部焊缝的X光照片
最亮的颜色赋予一种颜色，其余的一种。
Pseudocolor Image Processing for the visual inspection of weld crack, the human error rates would be lower.

## Slide 29
Pseudocolor Image Processing
Intensity Slicing 强度分层
8种颜色，怎么做的？

## Slide 30
Pseudocolor Image Processing for Rainfall Detection
Each pixel in these images represents a physical land area whose size depends on the resolution of the sensors.
传感器降雨量分布图

## Slide 31: 函数映射基本原理
仿照对温度的描述方式，当温度比较低，我们会想到蓝色（又称冷色调）。
当温度较高的时候，会想到红色（又称暖色调）。
根据人感官上的这一特性，可以将亮度低的映射为蓝色，亮度高的映射为红色。

## Slide 32: 映射关系
按照前面的映射关系，最终可以获得灰度与彩色的对应关系如下图所示。
可以看到，经过综合之后，颜色与光照强度相关。

## Slide 33
Gray level to color transformation for achieving a wider range of pseudocolor enhancement results.
Transform function
可以按照如下所示的映射关系进行伪彩色处理。
255
0 63 127 191 255
f
gR
255
0 63 127 191 255
f
gG
255
f
gB
0 63 127 191 255
灰度级到彩色转换

## Slide 34
Bottom Details of the Train.
火车底部的细节增强

## Slide 35: 灰度级到彩色转换
可以将256灰度级的图象转换为伪彩色图像。
0 0<=f<=63
0 64<=f<=127
R(x,y)= 4f(x,y)-512 128<=f<=191
255 192<=f<=255
255-4f(x,y) 0<=f<=63
G(x,Y)= 4f(x,y)-256 64<=f<=127
255 128<=f<=191
1023-4f(x,y) 192<=f<=255
255 0<=f<=63
B(x,y) = 511-4f(x,y) 64<=f<=127
0 128<=f<=191
0 192<=f<=255
Gray level to color transformation for achieving a wider range of pseudocolor enhancement results.

## Slide 36
灰度级到彩色转换

## Slide 37: Example

## Slide 38
Notes: Matlab demos
-Toolboxes
graphics\plots of complex function

## Slide 39
Notes: Matlab demos
-Toolboxes
graphics\plots of complex function

## Slide 40
Notes: Matlab demos
-Toolboxes
graphics\plots of complex function

## Slide 41
Notes: Matlab demos
-Toolboxes
graphics\plots of complex function

## Slide 42
Notes: Matlab demos
-Toolboxes
graphics\plots of complex function

## Slide 43
Notes: Matlab demos
-Toolboxes
graphics\plots of complex function

## Slide 44
Notes: Matlab demos
-Toolboxes
graphics\3d surface plots

## Slide 45
Notes: Matlab demos
-Toolboxes
gallery\knot

## Slide 46
Notes: Matlab demos
-Toolboxes
gallery\klein II

## Slide 47
Notes: Matlab demos
-Toolboxes
gallery\cruller

## Slide 48
Notes: Matlab demos
-Toolboxes
gallery\hoops

## Slide 49
Notes: Matlab demos
-Toolboxes
gallery\slosh

## Slide 50
Notes: Matlab demos
-Toolboxes
gallery\slosh

## Slide 51
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 52
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 53
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 54
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 55
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 56
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 57
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 58
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 59
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 60
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 61
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 62
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 63: Pseudocolor-Color Processing 伪彩色处理

## Slide 64
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 65
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 66
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 67
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 68
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 69
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 70
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 71
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 72
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 73
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 74
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 75
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 76
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 77
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 78
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 79
Notes: Matlab demos
-Matlab
graphics\image colormaps

## Slide 80
看见声音?
Notes: Matlab demos
-Toolboxes
graphics\visualizing sound

## Slide 81
看见的声音
Notes: Matlab demos
-Toolboxes
graphics\visualizing sound

## Slide 82
看见的声音
Notes: Matlab demos
-Toolboxes
graphics\visualizing sound

## Slide 85
Motor Activation
1 Hz 2 Hz 3 Hz
Schlaug, et al, 1995,
Harvard Medical School and Beth Israel Hospital
Right Index Finger Movement
Notes: 食指
motor [ˈməutə]
n.发动机，电动机

## Slide 86
FLASH
注意一种武器喷出的彩条

## Slide 88
目 录
伪彩色处理
假彩色处理

## Slide 89: False-Color 假彩色
一幅彩色图像到另一幅彩色图像
Color to color transformation for achieving a wider range of pseudocolor enhancement results.
彩色到彩色转换。
Notes: false [fɔ:ls]

## Slide 90
原图
Notes: Image\img\art\lip.jpg.psd

## Slide 91
假彩色处理
用计算机上口红
Notes: Image\img\art\lip.jpg.psd

## Slide 92
假彩色处理
给舌头上口红？
Notes: Image\img\art\lip.jpg.psd

## Slide 93
Gray Level to Color Transformation Used in Multi-Spectral Image Processing
多光谱图像处理
It is often of interest to combine several monochrome images (which are formed by different spectrum band) into a single color composite.多幅灰度图像到一幅彩色图像.

## Slide 94
(a)-(d) show four spectral satellite images: blue, green, red, and near-infrared. (e) is the full-color image obtained by combining the first three images into a RBG image. (f) is the combination of (a), (b) and (e). Notation: near-infrared band is strongly responsive to the biomass components of a scene.
(a)
(b)
(c)
(d)
(e)
(f)
Potomac River
华盛顿特区的蓝、绿、红，近红外，r+g+b, n+g+b图像。浅蓝-建筑，红-生命。

## Slide 95
The type of processing just illustrated is quite powerful in helping visualize events of interest in complex images, especially when those events are beyond our normal sensing capabilities.
Red: newly ejected materials
Yellow: elder sulfur deposits.
木星的多组传感器的多光谱图像
红色火山岩浆，黄色，硫沉积。

## Slide 96
Multispectral Tissue Classification
T1
T2

3D Histogram
Segmented
Image
Notes: X CT 核磁

## Slide 97
Notes: Matlab demos
-Toolboxes
image processing\Landsat color composite

## Slide 98
Notes: Matlab demos
-Toolboxes
image processing\Landsat color composite

## Slide 99
Notes: Matlab demos
-Toolboxes
image processing\Landsat color composite

## Slide 100
Notes: Matlab demos
-Toolboxes
image processing\Landsat color composite

## Slide 101
Notes: Matlab demos
-Toolboxes
image processing\Landsat color composite

## Slide 102: Demonstration
探测仪器发现月球水资源 40陨坑含六亿吨水_资讯_MSN中国.htm(Word edition)
CATDOG.AVI
terminator1.avi
Notes: 伪彩色
假彩色
假彩色
infrared [ˌinfrəˈred]
a.红外线的

## Slide 104: 作业(1)
1 已知一幅图像为

## Slide 105: 作业(1)续
分别对其进行如下处理：
（1）对其进行线性对比度展宽
（2）对其进行非线性动态范围调整
（3）对其进行直方图的均衡化处理
（4）比较以上三种方法对该图像的处理效果。
(2)~(4)可自选，做了加分

## Slide 106: 作业(2)
2 什么是直方图均衡化与直方图规定化？
<可自选，做了加分>

## Slide 107: 第三章 图像增强
童立靖
北方工业大学计算机学院
tong_lijing@163.com